## Slide 1: Introduction to CapSense in ModusToolbox
Bragadeesh Viswanathan
Applications Engineer
21st May, 2020

## Slide 2: Agenda
Introduction to CapSense technology
Self-Capacitance vs Mutual Capacitive sensing
High Level Hardware Architecture
Basic terminologies
CapSense Tuning
CapSense Middleware library
CapSense Configurator in ModusToolbox 2.x
Demo Project
CapSense Data Structure
CapSense Tuner GUI
Advanced Topics

## Slide 3: CapSense Technology
CapSense technology measures changes in capacitance between a plate (the sensor) and its environment to detect the presence of a finger on or near a touch surface
Features:
  Robust touch sensing
  Liquid tolerant operation
  Low electromagnetic interference (EMI) performance
  SmartSense™ Auto-Tuning technology
  Low power consumption
  Wide operating voltage range (1.71 V – 3.6 V) – PSoC 6
  Proximity sensing

## Slide 4: CapSense Sensors
Cp
Buttons
Matrix Buttons
Linear Slider
Radial Slider
Touchpad/Trackpad
Proximity sensor

## Slide 5: Self Capacitance vs Mutual Capacitance
Self Capacitance
Mutual - Capacitance
Cm - dCm
Cp
Cm
Cf + Cp

## Slide 6: When to use CSD , When to use CSX
Parameter/ Requirement | CSD | CSX
Pin constraints | Requires more pins | Requires Less pins(1)
High Cp designs |  | 
Proximity sensing |  | 
Overlay thickness | Thick overlays | Thin overlays (1 - 4 mm)
Liquid tolerance |  | (2)
Multi touch performance in matrix buttons | (3) | 
Spring sensors |  | 
VDD noise | (4) | 
(1) If sensors required is greater than 7. If there are X * Y sensors requirement, CSX requires only X + Y GPIO whereas CSD requires X * Y GPIO
(2) CSX + CSD for liquid tolerance. It is a special firmware. Contact our community support for further information.
(3) Ghost touch – (wrong reporting of fingers upon multi-touch)
(4) IDAC sourcing mode

## Slide 7: CapSense block - CSD
Each GPIO has a switched-capacitance circuit that converts the sensor capacitance into an equivalent current
An analog multiplexer then selects one of the currents and feeds it into the current to digital converter
The current to digital converter is similar to a sigma delta ADC. The output count of the current to digital converter, known as raw count, is a digital value that is proportional to the self-capacitance between the electrodes.

## Slide 8: CapSense – Basic terminologies
RawCounts
  Digital count value that is proportional to the self-capacitance between the electrodes in case of CSD and Mutual capacitance between electrodes in case of CSX
Baseline
  Filtered rawcounts at no touch condition
Difference Counts
  RawCounts(with touch) – Baseline (Signal)
Signal to Noise ratio
  Ratio of CapSense signal to CapSense noise. Recommended SNR is 5 : 1

## Slide 9: CapSense Tuning
Why should you tune sensors?
Reliable touch detection
Power consumption
Response time
Achieving Noise Immunity
Less Emissions

## Slide 10: CapSense Tuning – SmartSense vs Manual Tuning
SmartSense Autotuning:
  All parameters – set by component
  Reduced design cycle time and easy to use
  Limitations on memory and supported parasitic capacitance
  Less control over performance
Manual Tuning:
  Strict control over parameter settings such as response time, power consumption and noise immunity.
  Higher parasitic capacitance designs

## Slide 11: CapSense Middleware Library
The CapSense Configurator tool, which is a configuration wizard to create and configure CapSense widgets
API to control the design from the application program.
The CapSense Tuner tool for real-time tuning, testing, and debugging, for easy and smooth designing of human interfaces on customer products

## Slide 12: CapSense Configurator and CapSense Tuner GUI

## Slide 13: CapSense Configurator
Used to create and configure CapSense widgets
Generate code to control application firmware

## Slide 14: Demo Project – CapSense Initialization
Include cycfg_capsense.h to include CapSense Middleware and Configurator settings into your project
Initialize CapSense
  CapSense interrupt configuration
  Initialize CapSense hardware
  Initialize CapSense interrupt
  Enable CapSense interrupt
  Initialize CapSense firmware modules

## Slide 15: Demo Project – CapSense Scanning and Processing results
Application for ever loop
Is CapSense Busy?
Process Widgets
Process Touch
Trigger Scan
No

## Slide 16: Demo Project – Check Widget Status
Cy_CapSense_IsSensorActive()
  Reports whether the specified sensor in the widget detected touch.
Cy_CapSense_GetTouchInfo()
  Reports the details of touch position detected on the specified touchpad, matrix buttons or slider widgets.
Similar APIs
  Cy_CapSense_IsWidgetActive()
  Cy_CapSense_IsProximitySensorActive()
  Cy_CapSense_IsAnyWidgetActive()

## Slide 17: CapSense Data Structure
  The Data Structure is the only data container in the CapSense middleware.
  It serves as storage for the configuration and the output data.
  All CapSense modules use the data structure for the communication and data exchange.
  Data is split between RAM and Flash to achieve a reasonable balance between resources consumption and configuration / tuning flexibility at runtime and compile time

## Slide 18: Demo Project – Adding Tuner Support using EZI2C interface
Initialize an EZI2C interface to communicate with CapSense Tuner GUI
Expose cy_capsense_tuner structure as the read/ write buffer in EZI2C interface

## Slide 19: Demo Project – Adding Tuner Support using EZI2C interface
Calling Cy_CapSense_RunTuner() from the application is optional.

## Slide 20: CapSense Tuner GUI
The CapSense Tuner tool for real-time tuning, testing, and debugging, for easy and smooth designing of human interfaces on customer products

## Slide 21: CapSense Tuner GUI – View CapSense raw data

## Slide 22: CapSense Tuner GUI – Change hardware/ software parameters

## Slide 23: CapSense Tuner GUI – SNR Performance

## Slide 24: Advanced Topics – Firmware filters
IIR filter - Eliminates high-frequency noise
Median filter - Eliminates spike noise.
Average filter - Eliminates periodic noise
Limitations:
Increases memory consumption depending on filter
IIR filter slows down response
Increases processing time and hence power consumption

## Slide 25: Advanced Topics – Multi Frequency Scanning (MFS)
MFS is used to prevent false touch detection in the presence of external noise at a particular frequency
Each sensor is scanned with three different frequencies
Median filter is applied on the results to eliminate noise

## Slide 26: Advanced Topics – Multi Frequency Scanning
Points to consider when using MFS
  Enabling MFS increases RAM usage by three times approximately
  Increases the sensor scan duration by three times
  The SmartSense (Full Auto-Tune) and the Multi-frequency scan features are mutually exclusive
  Use CapSense Tuner GUI to view the rawcounts for three different channels.

## Slide 27: Advanced Topics – Pipeline scanning using low level APIs
Custom scanning sequence
Reduce the total scan/ process time
Increase the refresh rate
Decrease the power consumption

## Slide 28: Advanced topics - Liquid tolerance in CapSense designs
When hatch fill around the sensor is grounded, the increase in raw count when a liquid droplet falls on the sensor surface may be equal to the increase in raw count due to a finger touch. In such a situation, sensor false triggers might occur.

## Slide 29: Liquid tolerance in CapSense designs - Shield Electrode
The driven-shield signal is a buffered version of the sensor-switching signal
It has the same amplitude, frequency, and phase as that of sensor switching signal
Buffer provides sufficient current for the driven-shield signal to drive the high parasitic capacitance of the hatch fill
The increase in raw count when a water droplet falls on the sensor will be very small.

## Slide 30: Advanced topics – Built in Self Test (BIST)
Available from CapSense MW 2.10 (to be released soon…)
HW Tests – To confirm the CSD block and sensor hardware (external to chip) function correctly:
  Chip analog-routing verification
  Pin faults checking
  PCB-trace opens / shorts checking
  Sensors capacitance measurement
  VDDA measurement.
FW Tests – To confirm the integrity of data used for decision-making on the sensor status
  Global and widget specific configuration verification
  Sensor baseline duplication
  Sensor raw count and baseline are in the specified range.

## Slide 31: Advanced Topics - Gestures
Supports one-finger and two-finger gestures on Sliders and touchpad.

## Slide 32: Advanced Topics - Gestures
Use the high level function, Cy_CapSense_DecodeWidgetGestures() to process all gestures for a specified widget.
Gesture detection functionality requires a timestamp for its operation. The timestamp should be initialized and maintained in the application program prior to calling this function.
Call Cy_CapSense_IncrementGestureTimestamp() periodically from the application layer or register a periodic callback such as SysTick to keep the timestamp updated.

## Slide 33: Resources
PSoC® 4 and PSoC 6 MCU CapSense® Design Guide
Cypress CapSense Middleware Library
ModusToolbox® Software Environment
ModusToolbox™ CapSense® Tuner Guide
ModusToolbox™ CapSense® Configurator Guide
Code Examples: Github repository