## Slide 1
ModusToolbox Software 2.0 An Overview and Introduction
Dheeraj Kamath - Applications Engineer
WW 20 12

## Slide 2
Introduction
Core Tools
  What they are and where to get them
  The make infrastructure and how it works (high level)
  How you create a project
Software Enablement
  BSPs, HALs, PDLs and other libraries
Supported Ecosystems
Agenda

## Slide 3: Introduction

## Slide 4: What is ModusToolbox Software?
It is a collection of tools and libraries
It is compatible across environments (Linux, macOS, Windows)
Configuration tools
Low-level drivers
Middleware libraries
Operating system support
ModusToolbox IDE
What does it include?

## Slide 5
Comprehensive
  it has the resources you need
Flexible
  you can use the resource in your own workflow
Atomic
  you can get just the resources you want
Design Goals

## Slide 6: What is in the MTB Installer?
Build system infrastructure
Configurators and tools
ModusToolbox IDE
Note: Installer does not include enablement software such as
driver libraries or middleware

## Slide 7: Where is the SDK?
It is on GitHub as a collection of independent repositories
https://github.com/cypresssemiconductorco/
It also provides libraries to be used in particular ecosystems
  MCU and Bluetooth SOC ecosystem – PSoC6, Wi-Fi, Bluetooth and BLE
  Mbed OS ecosystem – Mbed OS, TLS, Cloud Services
  Amazon FreeRTOS ecosystem – FreeRTOS kernel, AWS libraries, AWS Cloud Services

## Slide 8: Core Tools

## Slide 9: Core Tools
Build Infrastructure
Configurators and tools
Utilities
ModusToolbox IDE

## Slide 10: Build Infrastructure
What does it do?
  creates a project
    either a folder that contains all the files, or a ModusToolbox IDE project
  creates an executable
  provides debug capabilities
A makefile defines everything required for your project, including:
  the target hardware (board/board support package to use)
  the libraries to use for the project
  the build tools to use
  compiler/assembler/linker flags to control the build
In MTB 1.1 a similar concept in a file called modus.mk – that is gone
New makefile is called, get this, makefile 

## Slide 11: Build Infrastructure
You set values for variables in the makefile
You invoke the makefile
Three ways
  From the command line
  Use a new tool called Project Creator
    just does that, doesn’t compile or build
  Use the ModusToolbox IDE
Managing the makefile is documented in KBA229177

## Slide 12: Create a Project
In MTB IDE – you get an actual Eclipse-based project
  Use the New Application wizard
  No device selection, it is boards only
Project Creator
  It is the “New Application” wizard without the IDE
  You get a project folder with all the files
Command Line
  make getlibs (covered in upcoming slides)
  You get a project folder with all the files
Behind the scenes – all three approaches invoke make getlibs
  That’s what does the real work
  On the command line it’s explicit, otherwise implicit/hidden

## Slide 13: Create a Project (using ModusToolbox IDE)

## Slide 14: Create a Project (using Project Creator)
Tool available under: “ModusToolbox\tools_2.0\project-creator”

## Slide 15: Autodiscover and Project Creation
When creating a project, it starts in the folder containing the makefile
It creates a new folder (based on project name) and copies all required resources into the project folder
Template project
(fetched from Github / imported from local copy)
Your project
(created in your workspace directory)

## Slide 16: Autodiscover and Project Creation
All files appear in a project folder
  Using Project Creator, wherever you specify
  Using the IDE, in the Eclipse workspace
If you use the IDE, you also get a project file

## Slide 17: Autodiscover and Project Creation
Build system automatically discovers all .c, .h, .cpp, .s, .a, .o files in the makefile tree
  They are replicated in the project folder
You can add files that reside outside the makefile folder
  add another directory using the CY_SHAREDLIB_PATH variable
  You can explicitly list files in the SOURCES and INCLUDES make variables
  Example:
  INCLUDES=../MySource1 ../MySource2
  SOURCES=$(wildcard ../MySource1/*.c) $(wildcard ../MySource2/*.c)

## Slide 18: Libraries, .lib Files, and make getlibs
Add a library (e.g. middleware) by using a .lib file
You create a .lib file for each library you want to use – this is what’s in the file
  https://github.com/cypresssemiconductorco/emwin/#release-v5.48.1
  The last part of the URL is a git tag that specifies a particular commit I want to use
  A release tag never moves, so you can point your app to a stable, known-good release
  Instead of a tag, you can use an actual commit hash
make getlibs
  Finds each .lib file
  Reads it
  Clones the repository
  Checks out the code for the specific commit
  Adds those files to the libs folder in the new project folder

## Slide 19: Library Manager
Stand alone tool or inside the IDE
Add, remove, change version of any library
  You can pick a BSP!
To retarget an application to a new kit
  Open the Library manager
  Pick the new kit
The new kit must support the same features/functionality but…
  All BSPs use a consistent set of definitions
Library manager updates the makefile

## Slide 20: Create an Executable
Build infrastructure provides several variables you use to control the build
MTB Installs GNU Arm toolchain, that’s the default

## Slide 21: Building Code from Within the IDE
A build command in the IDE wraps around make build from the command line
The “standard” Eclipse compiler build settings are all gone
  To change build settings, you edit the makefile. Build behaves precisely the same regardless of environment

## Slide 22: Program and Debug
the application creation process generates launch configurations

## Slide 23: Configurators and Tools
Introduces the concept of BSP Configurator and Library Configurator
Some changes in storing data
  It is not all in the design.modus file
There are two GeneratedSource folders in different places

## Slide 24: New Configurators and Tools
Configurator or Tool | Description
seglcd-configurator | Configure a generic LCD Direct Segment Drive controller for a variety of LCD glass at different voltage levels with multiplex ratios up to 16x.
project-creator | Create a new application project. This tool is a stand-alone version of the IDE wizard, available as a GUI and a command-line tool (CLI).
cype-tool | The power estimator tool provides an estimate of the power consumed by a target device.
library-manager | Select which library (including BSPs) and which version of each you want to include. Updates the makefile based on your choices.

## Slide 25: Utilities
Commonly used utilities that are required for application development

## Slide 26: ModusToolbox IDE
100% Optional
The command line infrastructure behind this makes that so
For the IDE, the make infrastructure also creates debug configurations

## Slide 27: Software Enablement

## Slide 28: What Have We Got?
Aimed at three key ecosystems
  PSoC 6 MCU and Bluetooth SoC ecosystem development
  Mbed OS ecosystem development
  Amazon FreeRTOS ecosystem development
These broad categories
  Low-level resources
  Middleware
  BSPs
  Code examples

## Slide 29: Low-level Resources

## Slide 30: Peripheral Driver Library (PDL)
Low level library for interacting with hardware
Simplifies software development
Extensive set of peripherals available
  Simplifies access to the low level drivers
  One call will work for drivers other than the PDL
  Does not do everything the PDL can do
  Takes care of resource allocation
Hardware Abstraction Layer (HAL)

## Slide 31: Board Support Package (BSP)
Common language for commonly used peripherals
BSP = a board/kit
  You can make your own and be discoverable
Includes any low-level resources (e.g. the PDL library for a PSoC 6 kit)
Has common macros for board peripherals (e.g. the RGB LED)
Typically includes the design.modus file (sets up a default configuration for the kit)
Uses the HAL to configure the board

## Slide 32: HAL, BSP and PDL, what do you use?
BSPs use the HAL to configure boards
HAL is intended to be the future
  Makes the application device agnostic.
PDL and HAL are 100% compatible – you can mix and match
  But it’s possible to use both to configure the same thing (developer’s responsibility)
Intent is that configurator will flag which peripherals it uses
  So HAL won’t step on configuration code

## Slide 33: Middleware
Each Cypress library is available independently on GitHub
  Some ecosystem libraries just live in that ecosystem
Connectivity middleware
  BT SDK (WICED), AWS IoT, Wi-Fi, BLE
PSoC 6 middleware
  CapSense, USB Dev, Device firmware upgrade, etc.
Bottom line, there is a LOT
  Some work for multiple ecosystems
  Some are specific to a particular ecosystem
GitHub landing page for PSoC 6 Middleware

## Slide 34: Code Examples
All on GitHub!
In general, each example will live in its own repository
  exception for an example with multiple projects
Item | Details
All ModusToolbox Examples | A GitHub landing page with information about the examples and links to various collections.
Bluetooth SDK Examples | A single repository that contains all the BT SDK examples.
PSoC 6 MCU Examples | This search link displays a list of all MCU related examples.
AWS IoT Greengrass Examples | These repositories contain all the AwS IoT-related examples in the Mbed OS ecosystem.
AWS IoT Client Examples | 
Mbed OS Examples | This search link displays a list of all Mbed-OS examples on the Cypress GitHub site.

## Slide 35: Targeted Ecosystems

## Slide 36: PSoC 6 MCU and Bluetooth SOC Ecosystem
All low-level resources
Most if not all BSPs

## Slide 37: Mbed OS Ecosystem
All low-level resources
BSPs for Mbed supported boards
All PSoC 6 middleware
  CapSense, etc.
Support for AWS IoT inside Mbed

## Slide 38: Amazon FreeRTOS Ecosystem
All low level resources
Two BSPs Qualified
  CY8CPROTO-062-4343W
  CY8CKIT-062-WIFI-BT
No PSoC 6 MCU middleware
  E.g.CapSense
Rich set of middleware
  All from 3rd parties, not Cypress
  Amazon FreeRTOS Libraries

## Slide 39: Amazon FreeRTOS libraries
It is a rich ecosystem

## Slide 40: Resources
ModusToolbox User Guide
ModusToolbox Software Overview
Running ModusToolbox from the Command Line
Cypress Github Landing Page
Mbed OS Cypress Page
Amazon FreeRTOS Cypress Repo
Managing the Makefile in ModusToolbox